ATINA MANUAL

1) install USB driver

You should install the USB driver before updating R5 first time.

Power on your R5 and connect to PC by the USB cable, then your PC would detect one new USB device. Please follow the installation wizard and finish the installation.

2)run the ATINA application software

Select “NAND” and choose the .img file for updating your mobile

3)take off the battery from the R5 handset

4)connect the R5 to PC with the USB cable

5)take something like needle to press the button in the small hole on the right side of R5.

Please make sure the button is pressed tightly. If it is not pressed down, one charging indication would appear on R5 screen when the battery is inserted

6)click “Start flashing”

7)insert the battery to the R5, and flashing would start. Then you can loose the button in the small hole